## Slide 1: Programming
2016.5.02, PPR meeting
Damien Zufferey
Ongoing work with Martin, Stelios, Daniela, Ankur, Joseph, …

## Slide 2: Automated Software Verification
Proof
Counterexample
Spec.
Notes: “Beware of bugs in the above code; I have only proved it correct, not tried it.” Donald Knuth

## Slide 3: Bird's-Eye View of a Program
Input
Output
Servo servo;
servo.attach(9);
int v = analogRead(A0);
v = map(v,0,1023,0,180);
servo.write(v);

## Slide 4: The Program is Only Half of the Story
IR distance sensor
Continuous servo left
Continuous servo right
Servo holding the sensor

## Slide 5: Meanwhile in the Literature …
-alternating bisimulation and incremental input-to-state stability!
Let a
move in a 2D discrete grid...
Notes: Unfortunately, simple models and complex arguments only come with an expert in the loop.
Expert in the loop:
come up with a model
justify that the model corresponds to the

## Slide 6: Talos
Submitted to OOPSLA 16

## Slide 7: “Full Stack” Robot Compiler
React
Robot
Compiler
[Mehta et al. 14]
Verifier
Spec.
Control logic
Robot design
Software
Component
Manufacturing
Models
Parameter values
Satisfy spec. yes/no
Notes: Full stack but with simpler robots
Take advantage of 3D printing & co.

## Slide 8: Robot Compiler
Arm = Component()
Arm.addSubcomponent("l0", Link)
Arm.addSubcomponent("l1", Link)
Arm.addSubcomponent("l2", Link)
l = Arm.addParameter("length")
Link.setSubParameter(("l0", "length"), l)
Link.setSubParameter(("l1", "length"), l)
Link.setSubParameter(("l2", "length"), l)
Arm.addConnection(("l0","servo"),("l1","horn"))
Arm.addConnection(("l1","servo"),("l2","horn"))
Arm.addSubcomponent("c", ArmCtrl)
Arm.addConnection(("c", "alpha"),("l0","input"))
Arm.addConnection(("c", "beta"), ("l1","input"))
Kinematic pairs

## Slide 9: React
class ArmCtrl extends Component(alpha,beta) {
var counter = 0
every( 1000 ) {
counter match {
case 0 => counter += 1
publish(alpha, α₀))
publish(beta, β₀))
case 1 => counter += 1
publish(alpha, α₁)
publish(beta, β₁))
case 2 => counter += 1
publish(alpha, α₂))
publish(beta, β₂))
case _ => counter = 0
} } }
The software is a component.
Periodic loops as first class object.
Event driven interaction (ROS compatible)
Parameters
sensor[Int](IRsensor) {
case Int(i) => ...
}

## Slide 10: Verifier
React
Robot
Compiler
Verifier
Timed automaton
Nonlinear diff. eq.
Spec.
FOL formula
Backends
Hybrid model-checker
SMT solver (dReal)
Software verification control theory
inductive invariant barrier certificate
ranking function Lyapunov function
Notes: Automated verification

## Slide 11: Example: Edge Follower
Verifier
State-space coverage
Background subtraction

## Slide 12: Example: Avoiding Collision
Verifier
Counterexample
Spec:

## Slide 13: Controller/Robot Co-Synthesis
React
Robot
Compiler
Goal
Synthesis
Notes: A few words about rigidity
Verification = forward kinematic
Synthesis = reverse kinematic

## Slide 14: A peek inside the solver
[TACAS 16]
Interpolants in Nonlinear Theories over the Reals
with Sicun Gao

## Slide 15: Kind of Constraints
Discrete
Continuous
Polynomials
Transcendental functions
Differential equations

## Slide 16: -Satisfiability
+ nonlinear theory undecidable
+ nonlinear theory + -perturbations decidable
|
-sat
-sat / unsat
unsat
-satisfiability captures numerical computability.

## Slide 17: Branch-and-Prune ICP
ICP()
S.push()
while S not empty
S.top()
while ( … )
prune()
if
if small enough
return -SAT
else
branch()
S.push()
S.push()
return UNSAT

## Slide 18: Branch-and-Prune Example
A
B
Prune by B
Prune by A
Branch
Prune by A
Prune by B
Prune by A
Prune by B

## Slide 19: How do we get simpler models ?
Effector
Link
Link
Quantifier elimination
Very expensive
(doubly exponential, only for polynomials)

## Slide 20: How do we get simpler models ?
Effector
Link
Link
Craig interpolation
Better complexity: co-NP

## Slide 21: Interpolation as Weak Quantifier Elimination
Kinematic chain
Automatically extracted model:
30 variables
poly. deg. 2, trig. fct.
Interpolation
Simplified model:
5 variables
Only approximate ()

## Slide 22: Craig Interpolation
A
B
I
Let be unsatisfiable.
is an interpolant iff
is unsatisfiable
Usually, is computed from the unsatisfiability proof of .

## Slide 23: Proof from ICP:
ICP()
S.push()
while S not empty
S.top()
while ( … )
prune()
if
if small enough
return SAT
else
branch()
S.push()
S.push()
return UNSAT
Selecting
Prune = Split + ThLem
Split

## Slide 24: Selecting
(Weakening)

## Slide 25: Branching
(Split)

## Slide 26: Pruning by
(Split)
(Weakening)
(ThLem)

## Slide 27: ICP Produces Resolution Proofs
(Split)

## Slide 28: Interpolation Rules
(ThLem)
(Weakening)
(Split)

## Slide 29: Example
A
B

## Slide 30: Talos Summary
“Full stack” system
  Control logic + physical design
  Validation against specification and synthesis of parameters
  Runtime and manufacturing
Technical contributions (inside the verifier)
  More scalable algorithms for the SMT Solver
  New features, e.g., Craig Interpolation
Future work
  More scalable algorithms for the SMT Solver
  The environment
  Automatically going from continuous to discrete, compositional reasoning
Notes: !!! dReal is used at Toyota research !!!